## Slide 1: CG1112
Tutorial 1

## Slide 2: Part 1
Pi, Git & Complexity

## Slide 3: Q1. Comparing Rpi and Arduino
[Raspberry Pi] You have now used both a Raspberry Pi and Arduino. Find out the differences between these boards in the follow areas:
  Power Requirement (Voltage, Current for typical usage).
  Hardware Specification (CPU clock speed and runtime memory).
  Interfacing capabilities (to other devices, components, networking etc).
  Software environment
[For better consistency in discussion, please base your findings on Raspberry PI 3 model B and Arduino Uno.]

## Slide 4: Q1. Suggested Answer
 | Raspberry Pi 3 Model B | Arduino Uno
a | 5v, 800mA (bare board) | 3.3v, ~50mA
b | 1.2GHz x 4 (ARM processor quad core), 1GB SDRAM | ATmega328 (8-bit CPU, 16MHz clock speed, 2KB SRAM, 32KB flash storage)
c | 40 I/O pins, USB ports, HDMI port, Ethernet Port | 20 I/O pins, USB port for power and act as an additional serial port
d | Full fledge computer with an OS. Multiple programs can executes in parallel (or in time sharing mode). | Microcontroller that run only one task by default.
Are these fixed? No, The Uno can operate at a range of voltages.
Yes for now, but things will change when you learn about multi-threaded development.
Significant processing power for complex tasks

## Slide 5: Q1. Based on the above, suggest 1-2 scenarios where Pi is more suitable for deployment.
Since Pi is very much a fully functional computer, it is useful in cases where complex software is needed. E.g. running a mini-web server, streaming content through the network, etc.
Arduino is used when you have simpler tasks like motor control, sensor interface, etc. More powerful variations of the Arduino board, like the Mega, MKR series, are also very powerful and capable of similar tasks, but they don’t typically offer a PC-type UI.

## Slide 6: 2. Git
[Git] Consider the following scenario, suggest how to achieve the desired outcome by utilizing Git.
  You are the working on a solo C coding project.
  There is one function X in the project that has two possible implementations A and B (e.g. different algorithms, different data structure etc).
  You want to try both of the approaches separately.
Focus only on functionalities learned in the studio. Discuss the problems with this approach.

## Slide 7: 2. Suggested Answers
One possible way is to:
  Commit the original code without function X (say version 1.0).
  Implement the first approach A and commit as version 2.0a.
  Checkout version 1.0, then implement the second approach B and commit as version 2.0b.
  Check out version 2.0a or 2.0b as needed.
This is workable but very cumbersome especially when the alternative approaches are much bigger than a single function (e.g. consider the case where you need multiple commits for each version). Git support the branching function, where you can split off and maintain two separate lines of work. This is not covered in the studio / course, but you are encouraged to explore on your own.

## Slide 8: 2. What if we don’t want to branch and keep both implementations in the code.
One possible approach is to use Conditional Compilation with BUILD_FLAGS.
For example #define MAPPING_ALGO ASTAR -> in a header file
  #if(MAPPING_ALGO == ASTAR)
  …
  #else
  …
  #endif
Only 1 set of these conditions will be compiled into the final executable.
Different from run-time if-else checks.

## Slide 9: 3. Complexity
WorkA( 54321 * N );
  -> unitWork() is independent of N. Its always fixed at 567*N.
  -> Constant Time
  -> O(1)
void workA(int N)
{
int i;
for (i = 0; i < 567; i++){
unitWork();
}
}

## Slide 10: 3. Complexity
WorkB( 73 * N );
  -> unitWork() is dependent on N in a single-loop.
  -> O(73 * N)
  -> O(N)
void workB(int N)
{
int i;
for (i = 0; i < N; i++){
unitWork();
}
}

## Slide 11: 3. Complexity
WorkC( 5 * N );
  -> unitWork() is dependent on N in a nested loop.
  -> O((5 * N)2) = O(25 * N2)
  -> O(N2)
void workC(int N)
{
int i, j;
for (i = 0; i < N; i++){
for (j = 0; j < N; j++){
unitWork();
}
}
}

## Slide 12: 3. Complexity
WorkE( N );
[WorkE(N)]  [WorkE(N/2)]  [WorkE(N/4)]  ….  [WorkE( 0)]
The call is a 1D list with total floor(log2(N)) + 2.
Each call has 1 unit of work.
Total complexity = O( floor(log2(N)) + 2)  O(log2(N))
void workE(int N)
{
if (N == 0){
unitWork();
return;
}
workE( N / 2 );
unitWork();
}
Example: N = 8 -> floor(log2(8)) + 2 = 3 + 2 = 5
8
4
2
1
0
3
1
1
+
+
= 5

## Slide 13: 3. Complexity
WorkD( N );
[WorkD(N)]
[WorkD(N/2)] [WorkD(N/2)]
[WorkD(N/4)] [WorkD(N/4)] [WorkD(N/4)] [WorkD(N/4)]
…..
[WorkD(0)] ………. [WorkD(0)]
void workD(int N)
{
int i;
if (N == 0){
unitWork();
return;
}
workD( N / 2 );
workD( N / 2 );
for (i = 0; i < N; i++){
unitWork();
}
}

## Slide 14: 3. Complexity
16
8
8
4
4
4
4
2
2
2
2
2
2
2
2
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
N = 16, Depth = log2(16) + 2 = 4 + 2 = 6
4
1
1

## Slide 15: 3. Complexity
The call is a binary tree with height [floor(Log2(N)) + 2]
In this case, it is easier to note that each level has the same amount of work in total. e.g. Each of the WorkE(N/2) do N/2 work, so that level sum up to N/2 + N/2 = N, similarly for the WorkE(N/4) level, where each of the 4 calls do N/4 work  total N.
So, total complexity = O( N * height) = O( N * log2N )

## Slide 16: 4. Time and Space Complexity
Given a character strings of N characters, tally the frequency of occurrences for every characters and print out the answer.
Example: "ab!da!" (N = 6 characters) Output: a = 2 times b = 1 time ! = 2 times d = 1 time a = 2 times //note the result is printed for every characters in the ! = 2 times // input string, regardless of duplication.
Suggest two algorithms with the following restrictions:
a. Does not store any prior tally, i.e. recalculate the frequency for every characters
b. Use additional memory space to store the prior tally somehow.

## Slide 17: 4. Algorithm A
Approach A – Pseudo Code For I = 0 to N-1 Frequency = 0 Current = String[I] For J = 0 to N-1 if (Current is the same as String[I]) Frequency ++ Print result with String[I] and Frequency
Time complexity = O(N2)
Space complexity = O(1) (only I, J, Frequency and Current, independent of N)

## Slide 18: 4. Algorithm B
Approach B – Pseudo Code Array Frequency[256], initialized to all zeroes For I = 0 to N-1 Frequency[ String[I] ]++ //Use Ascii as index For I = 0 to N-1 Print Result with String[I] and Frequency[ String[I]]
Time complexity = O(N)
Space complexity = O(1) (only I, J, Frequency[256] and Current, independent of N)

## Slide 19: 4. Conclusion
In this case, Approach B is the obvious winner.
In general, time and space are two resources that are commonly in tradeoff relationship, i.e. we can spend more memory space in order to reduce the time spent or vice versa.
For example, there are many cases where we can do pre-processing on the data and store the information to help with future calculation.

## Slide 20: Part 2
Understanding Microcontroller

## Slide 21: 1. Microcontroller Register Size
How many bit microcontroller is this device?
What can you deduce from your answer?
Suggested Answer:
8 – bit Microcontroller.
It means that it can deal with 8-bit data at a time.
Indirectly implies that all its internal working registers are also generally 8-bit.

## Slide 22: 2. Operating Speed
What is the fastest speed at which this device can operate?
Can it be clocked even faster than that?
Suggested Answer:
20mHz
Possible to go faster, because manufacturers always give you the lower bound to be safe.
Many devices can actually run faster than that, but it is not recommended as it is NOT guaranteed by the manufacturer.

## Slide 23: 3. I/O Ports
How many I/O ports are there and what are their bus widths?
Suggested Answer:
  3 I/O ports
  PortB: 8-bits [7:0]
  PortC: 7-bits [6:0]
  PortD: 8-bits [7:0]

## Slide 24: 4. PortB Mapping
Note down the mapping of PortB pins to the actual Microcontroller Pins.
PB7 | PB6 | PB5 | PB4 | PB3 | PB2 | PB1 | PB0
10 | 9 | 19 | 18 | 17 | 16 | 15 | 14
Suggested Answer:

## Slide 25: 5. Understanding Multiplexing
What are PB7 and PB6 already used for in the Uno board?
Suggested Answer:
They are already connected to the external clock. So, they are no longer available for use as General Purpose I/O.

## Slide 26: The End!
Q & A