## Slide 1: CG1112
Tutorial 3

## Slide 2: Recap of Studio
DRV8833 – Dual H-Bridge Motor Driver
The H-Bridge design allows us to change the direction of the motor by controlling the switches.
When we change the inputs to AIN1 and AIN2, that’s what we are doing.

## Slide 3: Recap of Studio
Lets look back at the code:
void right_motor_forward(void)
{
TCCR0A = 0b10000001;
PORTD &= 0b11011111;
}
void right_motor_reverse(void)
{
TCCR0A = 0b00100001;
PORTD &= 0b10111111;
}

## Slide 4: Recap of Studio
How do we know which pins the OCOA and OCOB are mapped to?

## Slide 5: Recap of Studio
Is the PORTD assignment necessary?
PORTD &= 0b11011111;
Looking back at the datasheet for the DRV8833:
When one input pin is driving the motor, the other pin must be LOW.
In the AT328P, once we set the COMA1:0 bits to “00”, it reverts to normal port operation with the default LOW output.
In this case, it works even without the PORTD assignment.

## Slide 6: Part 1
PWM

## Slide 7: Q1. Understanding the PWM Module
a) We saw that the AT328p has 3 Timers capable of generating 6 individual PWM signals. Consider the following scenarios and describe how you will be able to resolve the challenges.
Describe a SW approach to generate a PWM signal that is not dependent on the HW PWM peripheral block within the microcontroller.

## Slide 8: Q1. Understanding the PWM Module
In the SW approach, we need to manually keep toggling the output pin based on the ON and OFF time for the required Duty-Cycle.
Pseudo-Code:
  Configure Pin as output
  Set as ‘1’
  Delay for ‘T-on’
  Set as ‘0’
  Delay for ‘T-off’
  Loop to Step 2.

## Slide 9: Q1. Understanding the PWM Module
What is the drawback of generating the PWM using this approach?
With this approach, the microcontroller is continuously executing the loop to generate the required PWM. As such, it cant do anything else more productive. Furthermore, if there are interrupts in the system, the timing characteristics for the PWM will also be affected.
When the peripheral block is used to generate the PWM, only the initial setup code needs to be executed. Subsequently, it is driven by the HW with minimal processing time in the Interrupts.

## Slide 10: Q1. Understanding the PWM Module
b) The microcontroller that you have to use for a particular project (not the AT328p) doesn’t have any PWM module. How can you still generate a PWM signal WITHOUT relying on the software-based approach that you did in Part A? (Recall HW-based solutions from EPP1)

## Slide 11: Q1. Understanding the PWM Module
One possible approach is to use the 555 Timer to generate the required PWM signal. The PWM and the Duty Cycle can be varied by adjusting the RA and RB value of the circuit.
* You have learnt this in EPP1. You can refer to Week6 Studio1 from EPP1 to refresh your memory.

## Slide 12: Q1. Understanding the PWM Module
c) You feel that the approach in the earlier part is going to add additional cost to your project and you decide to stick with the AT328P. You require a very low-frequency PWM signal and even with the largest pre-scaler setting, the period is still too high. How will you be able to generate a PWM signal with the required period?
Propose at least THREE different approaches that can involve both HW and SW.

## Slide 13: Q1. Understanding the PWM Module
Option A:
It is possible to clock the device using an external clock on T0 pin.

## Slide 14: Q1. Understanding the PWM Module
Option B:
Another software approach would be to use the ISR to keep track of the number of Interrupts and then toggle the output pin accordingly. In this approach, we cannot allow the PWM block to control the pin directly. The ISR needs to handle it.

## Slide 15: Q1. Understanding the PWM Module
Option C:
Consider using a higher-bit timer. In the AT328P, we have Timer 1, which is a 16-bit timer/counter.

## Slide 16: Q2. Timer Interrupts
In the studio, you were driving a single motor. If we were to drive both Motors concurrently, one possibility is to use both Timer 0 and 2.
Assume that both Timer blocks are configured to use Interrupts and that the microcontroller was executing code in your loop() routine prior to the interrupts.

## Slide 17: Q2. Timer Interrupts
a) If both these interrupts were to be triggered at the same time, what would be the sequence of execution?
Main()
Timer 2 ISR
Timer 0 ISR
Main()
Context Switch
Recall: Interrupt Priority

## Slide 18: Q2. Timer Interrupts
b) If Timer 0 triggered the interrupt just before Timer 2, what would be the sequence of execution?
Main()
Timer 0 ISR
Timer 2 ISR
Main()
By default, Nested Interrupts are disabled. When Timer 0 triggers the interrupt first, the controller will jump to Timer 0 ISR and start executing. When Timer 2 triggers, the event is captured by the flag, but the current ISR will complete execution and perform a context switch to the loop(). At this time, the flag will cause the jump to the Timer 2 ISR.

## Slide 19: Q2. Timer Interrupts
What if nested interrupts were enabled?
Main()
Timer 0 ISR
Timer 2 ISR
Main()
Timer 0 ISR
T0 ISR pre-empted by T2
T0 ISR resumes

## Slide 20: Part 2
Timers & Interrupts

## Slide 21: Q1. Interrupts
We wish to read a block of 16384 bytes from a disk drive.
  We have the following program that reads from the drive using polling.
byteCount=16384;
i=0;
while(byteCount>0)
{
while(!DRIVE_READY);
buffer[i++]=DRIVE_DATA_LATCH;
byteCount--;
}

## Slide 22: Q1. Interrupts
Assuming that our microprocessor runs at 50 MHz and the drive transfers data at a rate of 1 megabyte per second (1 MBPS), how many clock cycles are spent on polling between each byte? How many clock cycles are spent in total on polling?

## Slide 23: Q1. Interrupts
How many clock cycles are spent on polling between each byte?
Answer:
1 MBPS -> 1000000 bytes /sec -> 1byte / us
F = 50Mhz -> T = 20ns
1us -> 1us / 20ns clocks -> 50 clocks
I take 50 clk cycles to complete the transfer of 1 byte

## Slide 24: Q1. Interrupts
How many clock cycles are spent in total on polling?
byteCount=16384;
i=0;
while(byteCount>0)
{
while(!DRIVE_READY);
buffer[i++]=DRIVE_DATA_LATCH;
byteCount--;
}
The code spends 50 clock cycles per byte, at this line, waiting for data to be transferred from the drive to the microprocessor.
The loop is run for 16384 times
-> Total time spent polling
= 50 * 16384
= 819,200 cycles.

## Slide 25: Q1. Interrupts
We now use interrupt driven I/O instead, and an interrupt is triggered each time a byte arrives from the drive. Assuming that it takes 50ns to process each interrupt, how many clock cycles are spent processing each interrupt? How many clock cycles are spent in total when we transfer 1 block from the drive?
Answer:
50ns = 2.5 clock cycles. Each byte triggers an interrupt.
Time taken to process the entire block is
-> 2.5 * 16384 = 40,960 cycles.

## Slide 26: Q1. Interrupts
There is a 3rd transfer mode not covered in lectures called Direct Memory Access or DMA, where a separate piece of hardware called the DMA Controller or DMAC completely takes over the transfer of data and sends an interrupt when the transfer is complete. The downside is that it takes a little bit of time to set up the transfer.
The DMA operation is not part of the CG1112 syllabus. You will learn more about it CG2271.
The basic idea of the DMA is that it has the ability to take control of the address and data bus to move data around, while freeing up the CPU to carry on with other tasks.

## Slide 27: Q1. Interrupts
Assuming it takes 1000ns to set up a DMA transfer and 200ns to process the DMA interrupt, how many clock cycles are spent in total when transferring one block from the disk drive?
Answer:
Total = 1000+200 = 1200 ns = 60 cycles

## Slide 28: Q2. Interrupts
Repeat Question 1, but with a block size of 8 bytes instead of 16384 bytes. Comment on the relative efficiencies of polling, interrupt driven I/O and DMA. From your answers comment on why devices like the keyboard, mouse and UART port do not use DMA.
Polling:
Each byte still takes 1 microsecond or 50 cycles.
Total number of cycles taken is 50*8 = 400 cycles.
Interrupts:
Each interrupt still takes 2.5 cycles. Total time = 8*2.5 = 20 cycles.

## Slide 29: Q2. Interrupts
DMA:
No matter what the block size is it will always take 60 cycles.
Since DMA set-up and interrupt processing time is independent of block size, DMA is not efficient for small block sizes. This means that “character devices” like the mouse, keyboard and UART port do not benefit from the advantages of DMA.

## Slide 30: Q3. Timers
We are given the following contents of TCCR1A and TCCR1B, and OCR1A holds the value of 247. Given that TCNT1 is initially 0, that we are operating Timer 1 in CTC mode, and that all interrupt flags in TIMSK1 and SREG are properly set:
TCCR1A = 0b01010000;
TCCR1B = 0b00001100;
WGM13:10
COM1A1:0,COM1B1:0
CS12:0

## Slide 31: Q3. Timers
What is the interval between which TIMER1_COMPA_vect is triggered?
Answer:
The prescalar is 0b100 which is 256.
At 16MHz, the period is 256/16000000 = 16 us.
The period therefore is (247 + 1) * 16 us = 3.968 ms.

## Slide 32: Q3. Timers
Sketch the waveform on OC1A.
Answer:
There is a match approx. once per 4 ms, and the COM1A0 and COM1A1 bits are 0b01, which is a “toggle on match”.
Hence we get a square wave of period of about 8 ms.
~8ms
~4ms

## Slide 33: Q4. Timers
We want to trigger TIMER0_COMPA_vect on Timer 0 once every 650 us (microseconds) in CTC Mode. Complete the following table. Round up any cases where V is not an integer (e.g. 34.3 -> 35, 38.8 -> 39, etc).
Assume that the Atmega328P is being clocked at 20 MHz and that CLKIO is identical to the Atmega’s frequency.

## Slide 34: Q4. Timers
Note: To get the period we take P / 20000000, where P is the prescalar value.
Answer (e.g. for P = 64):
When P = 64,Resolution = 64 / 20000000 = 3.2us
To reach 650us, we need -> 650 / 3.2 = 203.125 counts of TCNT1
Rounding Up 203.125, we get 204
With OCR1A set to 204, we get a period of -> 204 * 3.2 = 652.8
This gives us an error of (652.8 – 650) / 650 * 100% = 0.43%

## Slide 35: Q4. Timers
Repeat the procedure for all the Prescaler value.
Prescalar | Period in us | V (no rounding) | V (rounding) | Actual period
CLKIO/1 | 0.05 | N/A | N/A | N/A
CLKIO/8 | 0.4 | N/A | N/A | N/A
CLKIO/64 | 3.2 | 203.125 | 204 | 652.8 us
CLKIO/256 | 12.8 | 50.78125 | 51 | 652.8 us
CLKIO/1024 | 51.2 | 12.6953125 | 13 | 665.6

## Slide 36: Q4. Timers
Based on the table above comment on which value of V gives the best accuracy. Why do you think this is so?
Answer:
Prescalar of 64 and 256 give the same accuracy while prescalar of 1024 gives very poor accuracy.
In general the smaller a prescalar is, the more accurate the timing would be. Of course this will also depend on the rounding error.

## Slide 37: THE END!
Q &A