## Slide 1: EPP2
Tutorial 5

## Slide 2: Part1
Serialization

## Slide 3: UART Link-Layer Protocol
1a. Show how odd and even parity bits works, and how they can be used to detect errors.
A “parity bit” is an extra bit that is set/cleared so that the total number of “1” bits sent is either odd or even.
Odd Parity: Parity bit is set so that the total number of 1 bits is odd.
E.g.: Data = 0b10010010 -> Parity = 0
Even Parity: Parity bit is set so that the total number of 1 bits is even.
E.g.: Data = 0b10010010 -> Parity = 1

## Slide 4: UART Link-Layer Protocol
1b. Explain why error detection with parity bits is not reliable, and what engineers can do to overcome/improve this lack of reliability.
Parity checking can only detect an odd number of parity errors.
0b00101100
With Even Parity
0b00101100 : 1
0b01001100 : 1
Transmission Channel
Tx Data
Rx Data
Parity is still correct due to Even number of errors
We need higher levels of checking like Checksums and CRCs.

## Slide 5: UART Link-Layer Protocol
1c. Sketch the frames for the following pieces of 8-bit data in 8N1, 8E1, 7O1 and 7E1 frame formats. Where you are using 7-bit frames, discard the most significant (left most) bit.
St – Start bit: High to low transition
S – Stop bit: A high bit
8N1: St-10110001-S
8E1: St-10110001-0-S
7O1: St-0110001-0-S
7E1: St-0110001-1-S
0b10110001
0b01010011
8N1: St-01010011-S
8E1: St-01010011-0-S
7O1: St-101011-1-S
7E1: St-101011-0-S

## Slide 6: Parity across Bytes
2. Note below that the row parity for byte 1 is wrong (there’s an even number of bits in an odd-parity system). The number of “1” bits in column b4 is also wrong. This tells us that bit 4 of byte 1 (the highlighted square) is wrong and should be flipped to a 1
Data bits -> | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0 | Parity (within byte)
Byte 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
Byte 2 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
Byte 3 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
Parity (across bytes) | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
You can actually detect more than one bit error, as long as there is no other error in the same column and row.

## Slide 7: Flow Control
3. Our lectures do not look at flow control. Explain how XON and XOFF, and CTS/RTS flow control work and the differences between them.
Flow control is a method that allows a receiver to tell a transmitter to stop sending so that it has more time to process the data already received, preventing buffer overflows.
XON/XOFF is software flow control, and makes use of special characters ASCII 0x13 for XOFF (corresponding to CTRL-S) and ASCII 0x11 for XON (corresponding to CTRL-Q).
Then the receiver cannot accept any more data it will send an XOFF, causing the transmitter to pause. When the receiver can receive further data, it will send an XON and the transmitter resumes.
(This behaviour is mimicked by many terminal programs where you can press CTRL-S to stop a screen from scrolling and CTRL-Q to resume scrolling)

## Slide 8: Flow Control
CTS/RTS is a hardware flow control that makes use of two additional hardware lines:
In unidirectional arrangements, RTS is “Ready to send” which is a hardware line that the transmitter asserts to tell the receiver that is has data. If the receiver is ok to receive the data, it will assert the CTS “Clear to Send” line, and the transmitter will begin sending.
However today CTS/RTS works slightly differently: One end will use CTS to say that it is ready to receive, while the other side would assert RTS (often called “RTR” instead) to signal that it is ready to receive.

## Slide 9: Data Rates
4. How long does it take to transmit all 128 bytes in a buffer at 9600 bps? What implications does this have on how fast your program can write to your buffers?
128 bytes = 1024 bits.
128 bytes = 1024 bits. It would take 0.11 seconds to send over 9600 bps. If data is written too quickly into the buffers, either the new data is lost or data that hasn’t been sent yet is overwritten.
1024 / 9600 = 0.1066 0.11

## Slide 10: Data Rates
5. Explain the difference between bit rate and baud rate. Explain why bit rate can sometimes be much higher than baud rate.
Baud rate is the number of symbols (in the case of UART, a 5v symbol and a 0v symbol) that can be sent per second over a transmission line.
The bit rate is the total number of data bits that can be sent in one second.
Usually these two are the same (‘1’ sent as a 5v symbol and ‘0’ sent as a 0v symbol), but with special encoding schemes and data compression that bit rate can be higher than the baud rate.

## Slide 11: Data Rates
Modems in the past could send 9600 bps over a 2400 baud channel by using “Quadrature Amplitude Modulation” that uses two analog channels along the same telephone line to send 4 bits per symbol.
The later V34 standard could send 28800 bps by using “Trellis Coding”, while the V42 standard used compression to send up to 56.6 kbps.
QAM Signal

## Slide 12: Use of a Magic Number
6. The serializing code provided to you uses a magic number of 0xFCFDFEFF. What is the purpose of the magic number?
A “magic number” is a byte sequence that the receiver can use to detect if the current block of data actually constitutes a data packet, or it’s just simply a random sequence of bytes.

## Slide 13: Use of a Magic Number
In TComms Structure
#define MAGIC_NUMBER 0xFCFDFEFF
typedef struct comms
{
uint32_t magic;
uint32_t dataSize;
char buffer[MAX_DATA_SIZE];
unsigned char checksum;
char dummy[3];
} TComms;
comms.magic = MAGIC_NUMBER;
In Serialize
In DeSerialize
if(comms->magic != MAGIC_NUMBER)
{
// Print Error Message
return PACKET_BAD;
}

## Slide 14: Checksums
Derive the checksum for the following sequence of bytes:
0A 1C 42 3A
0A | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1C | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
XOR | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
42 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
XOR | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
3A | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0
XOR | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
Checksum = 0x6E

## Slide 15: Checksums
Explain how to use this checksum to check for errors.
The checksum 6E is attached to the byte stream to get:
0A 1C 42 3A 6E
The receiver will repeat the computation over the received bytes and compare the result with the checksum.
If the computed result does not match the attached checksum, an error has occurred.

## Slide 16: Checksums
The sequence in part a. was sent out by the transmitter but the receiver instead received:
09 1C 41 3A
Derive the checksum for this new sequence.
09 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
1C | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
XOR | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
41 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
XOR | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
3A | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0
XOR | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
Checksum = 0x6E
Bit-Flip

## Slide 17: Checksums
From your earlier answer, what is the main weakness of checksums?
Checksums can fail to detect errors if there is an even number of errors in a column.

## Slide 18: Part2
LIDAR

## Slide 19: Lidar Interface – Communication Modes
A communication session is always initialized by a host system, i.e. a MCU, a PC, etc. RPLIDAR itself won’t send any data out automatically after powering up.
If a data packet is sent from host systems to RPLIDARs, such a packet is called a Request. Once an RPLIAR receives a request, it will reply the host system with a data packet called a Response.
A fixed 0xA5 byte is used for each request packet, RPLIDAR uses this byte as the identification of a new request packet. An 8bit (1byte) command field must follow the start flag byte.
RPLidar’s Request Packet Format

## Slide 20: Lidar Interface – Communication Modes
All the response packets are divided into two classes: response descriptors and data responses.
If the current request received by RPLIDAR requires a response, RPLDAR will always send a response descriptor packet first and then send one or more data response packets based on the type of requests.
Only one response descriptor packet will be sent out during a request/response session.

## Slide 21: Lidar Interface – Communication Modes
The format of response descriptors is depicted in the following figure.
A response descriptor uses fixed two bytes’ pattern 0xA5 0x5A for the host system to identify the start of a response descriptor.

## Slide 22: Lidar Interface – Communication Modes
Request / Response Mode

## Slide 23: Lidar Interface – Communication Modes
Single Request – Multiple Response Mode
Another request

## Slide 24: Lidar Interface – Communication Modes
Single Request – No Response Mode

## Slide 25: LIDAR Interface
1 a) Describe the steps required to get the device information from the rplidar unit. Focus on the message format and meaning of the fields of the messages exchanged.
Method getDeviceInfo() at line 179, rplidar_driver.cpp
Send to RPlidar a command message (_rplidar_cmd_packet_t, line 55, rplidar_protocol.h) with the following fields:
syncByte (1 byte) | cmd_flag (1 byte) | Size (1 byte) | Data ( x bytes)
0xA5 (line 39, rplidar_protocol.h) | 0x50 (line 50, rplidar_cmd.h) | Not used in this command | Not used in this command

## Slide 26: LIDAR Interface
The Interface Table shows the command and response type information.

## Slide 27: LIDAR Interface
Receive a response message header (rplidar_ans_header_t, line 63, rplidar_protocol.h)
syncByte1 (1 byte) | syncByte2 (1 byte) | Size_q30_subtype (4 bytes) | Type (1 byte)
0xA5 | 0x5A | 30 bits to represent size of additional response data 20 bytes for device info | 0x4 (line 88, rplidar_cmd.h)

## Slide 28: LIDAR Interface
Receive the device info message (rplidar_response_device_info_t, line 149, rplidar_cmd.h)
Model (1 byte) | Firmware_version (2 bytes) | Hardware_version (1 byte) | SerialNumber (16 bytes)

## Slide 29: LIDAR Interface
1b) Describe the steps required to get the health information from the rplidar unit.
Send to RPlidar a command message (_rplidar_cmd_packet_t, line 55, rplidar_protocol.h) with the following fields:
syncByte (1 byte) | cmd_flag (1 byte) | Size (1 byte) | Data ( x bytes)
0xA5 (line 39, rplidar_protocol.h) | 0x52 (line 51, rplidar_cmd.h) | Not used in this command | Not used in this command

## Slide 30: LIDAR Interface
Receive a response message header (rplidar_ans_header_t, line 63, rplidar_protocol.h)
syncByte1 (1 byte) | syncByte2 (1 byte) | Size_q30_subtype (4 bytes) | Type (1 byte)
0xA5 | 0x5A | 30 bits to represent size of additional response data 3 bytes for health info | 0x6 (line 89, rplidar_cmd.h)

## Slide 31: LIDAR Interface
Receive the device info message (rplidar_response_device_health_t, line 156, rplidar_cmd.h)
Status (1 byte) | Error_code (2 bytes)

## Slide 32: Summary
Establishing a communication interface between multiple devices requires us to have a clear understanding on its data sizes, endianness, order (LSB/MSB first), voltage levels, bit/baud rate, etc.
For any other peripheral device that is connected to your processor, like the RPLidar, we must be able to establish a proper communication channel with it.
The protocol details must be given by the manufacturer. If they provide libraries, API’s, sample code, etc., then it makes our life a lot easier to integrate the device with our project.